## Slide 1
Ion Cyclotron and Lower Hybrid Cold Magnetized Plasma Modelling in ANSYS HFSS
J.Hillairet1, R.Ragona2, L.Colas1, W.Helou1, F.Bocquet3
2
3
1
Summary
Ion Cyclotron Resonance Frequency (2 straps, dipole phasing, 50 MHz)
Lower Hybrid Current Drive (6 rect. waveguides, 90° phasing, 3.7 GHz)
Results have been compared with the ALOHA code
Inhomogeneous losses have been added to dump wave power
  ANSYS HFSS allows using inhomogeneous (tabulated or analytical) and anisotropic media
  Can be used to model ICRF and LHRF coupling to tokamak edge cold plasma
  Default absorbing boundary conditions (radiation or PML) are not compatible with anisotropic dielectric tensors, so Ad hoc conditions must be defined manually
  Antenna S/Z-parameters have been successfully benchmarked with the codes ANTITER II and ALOHA
  ANSYS HFSS can be used to model 3D antenna-wave coupling problems to tokamak edge plasma.
Quadratic conductivity increase
Reflection coefficients
Spectrum
E-field
ne0
x
xplasma
0
ne
xcore
ne1
x
Equivalent dielectric + rad. BC
Cold-plasma + Ad hoc BC
No loss region
  In ICRH range of plasma parameters, P(x) values are >104  Leads to large computing resources (mesh & memory).
  Using a equivalent dielectric KD(x)=S - D as proposed in [A.Messiaen, R.Weynants, PPCF 53 (2011)] is a good/faster workaround for S-parameters evaluation.
  Inhomogeneous cold plasma or equivalent dielectric have been benchmarked with ANTITER II.
  Near-field pattern with cold-plasma is different from equivalent-dielectric
  Good agreement obtained on antenna Z-parameters
30 cm
Cut-off layer
Quadratic conductivity increase
  In the LH range of plasma parameters, plasma-facing dielectric tensor εr can be approximated by a diagonal tensor, with P < 0 if electron density ne is higher than the cut-off density nc.
|E|
|E|